## Slide 1: Olfactory Odor Source Localization Robot Using Deep Neural Networks
JA
By:
Mohammed Alajaji
Graduate Research Project
GRP- Summer 2022

## Slide 2
Warm-up
Introduction
Machine Learning (ML)
  Deep Neural Network (DNN)
  Convolutional Neural Network (CNN)
  Recurrent Neural Network (RNN)
  Transfer Learning (TL)
Data
Project Development
  Data Preprocessing
  Model Training
Results
Conclusion
Agenda

## Slide 3
Warm-up

## Slide 4
Robotics
  Mimics human or animal behaviors.
  Can be used in dangerous situations or in situations that humans or animals are not able to achieve.
  Perceives the world as a human does, with sight, smell, touch, taste, and hearing.
  Smell has not been sufficiently exploited in mobile robotics as the other senses.
Introduction

## Slide 5
Odor source localization (OSL) robot
  Was designed and constructed by Dr. Lingxiao Wang during his PhD research.
  Used different algorithms to trace and locate a plume and localize the chemical source.
  Was tested in real-world experiments.
Introduction

## Slide 6
Introduction
.
.
.
Robot
Sensors
ML Algorithm

## Slide 7
This Project is a continuation of Dr. Lingxiao Wang’s work.
It focuses on Machine Learning – Deep Neural Network (DNN).
Introduction
Notes: To investigate the generalization of the proposed DNN models, they are implemented in OSL tests with di↵erent search conditions, including varying robot initial positions, odor source locations, and environmental settings.

## Slide 8
CNN is preferable for two reasons:
  The query time of the machine learning model is predictable and unaffected by the size of the search area.
  It can learn other successful navigation methods from demonstrations with explicating specific search algorithms.
In this project, CNN and RNN are implemented to produce robot commands
Introduction

## Slide 9
Machine Learning - ML
ML has become the most popular and successful subfield of artificial intelligence.
Deep learning is the fastest-growing and the most significant subfield of machine learning.

## Slide 10
DNN has different models that serve various applications in different sectors nowadays.
DNN structure:
Deep Neural Network - DNN

## Slide 11
Suitable for forecasting time-series.
  Used for learning an effective navigation strategy and applying the learned knowledge to new environments.
  Preference for implementation to real-world applications due to the predictable query time.
  Fixed computational cost
CNN

## Slide 12
Powerful for modeling sequence data such as time series.
LSTM is an extension of RNN, which basically extends the memory.
LSTMs are used as the building blocks for the layers of RNN.
LSTMs assign data “weights” which help RNNs to either allow the input of new information, forget information, or assign it sufficient importance that can impact the output.
RNN

## Slide 13
TL enables us to utilize knowledge from previously learned tasks and apply them to newer, related ones.
The reason for using TL in this project is due to the lack of real data.
The learning process in TL can be faster, more accurate and/or require less training data.
Transfer Learning - TL

## Slide 14
Data
The data is the main component for the success of the machine learning models.
DNN needs as much data as possible to avoid overfitting and underfitting problems.
OSL robot data
  The OSL robot data was collected by Dr. Wang during his PhD research.
  Two types of OSL robot data are available: real data and simulated data.
  Only 120 samples of real data were collected
  6000 samples of computer simulated data were collected
  Three different methods were used to collect the data, namely moth-inspired, Bayesian-inference, and fusion methods.
Notes: because it is costly and time-consuming.

## Slide 15
Dataset
Computer Simulated Data
Real Data
Fusion Data (6000)
Moth-inspired Data (6000)
Bayesian-inference Data (6000)
Moth-inspired Data (120)
Bayesian-inference Data (120)
Fusion Data (120)
Data Collecting
Moth-inspired data was collected by mimicking the mate-seeking behaviors of the male moth.
Bayesian-inference is an engineering-based method.
Fusion data is a combination of the moth-inspired and Bayesian-inference methods

## Slide 16
The core idea of the project is to train a DNN model to provide accurate commands to the OSL robot to localize the odor source.
Project development steps:
  Data preprocessing
  Model training
  Real-world test
Project Development

## Slide 17
Data Preprocessing
Data preprocessing is a data mining technique used to turn the raw data into a format that is practical and effective.
Data preprocessing is very important part to convert the raw data into a well-readable format.
Data preprocessing consists of
  Dropping missing, inconsistent, and noisy values.
  Combining two or more features
  Reordering
  Normalization

## Slide 18
Data Preprocessing
Data preprocessing steps:
  visualize the raw moth-inspired data (Computer simulated data).

## Slide 19
Data Preprocessing
The raw data has 13 Features:
time (s) | It records the time in seconds from trail starts 0s until it ends 400s ≤.
windvx (m/s) | Wind velocity in x-axis direction.
windvy (m/s) | Wind velocity in y-axis direction.
con (mmpv) | Chemical concentration in the robot position
detection (1 or 0) | 1 when detecting a plume and 0 otherwise.
posx (m) | Robot position in x-axis
posy (m) | Robot position in y-axis
yaw (deg) | Robot heading angle
v (m/s) | Robot speed
yaw_c (deg) | Robot heading command
behavior | The robot’s behaviors (finding, tracing, tracking, …, etc.)
declare (1 or 0) | declare = 1 the robot reaches the odor source and 0 otherwise.
time_out (1 or 0) | 1 when the time reaches 400 s
termination (1 or 0) | Terminate the robot in two cases declare the odor source or the trials time = 400 s

## Slide 20
Data Preprocessing
2. Drop all the empty cells.
3. Drop unnecessary features ('declare’, 'termination’, 'time_out’, 'time’, 'posx’, 'posy’, 'yaw’, ‘v’, 'behavior').
5. Convert the robot heading commands “yaw_c” from negative values into positive by adding 360° to each element.
6. Convert the robot heading commands “yaw_c” from degree to radians.

## Slide 21
Data Preprocessing
7. Add two features which determine the robot heading commands in the x-axis and the y-axis.
8. Drop “yaw_c”
9. Normalize the entire dataset.

## Slide 22
1. Split the datasets into three sets:
    80% Training set.
    10% Validation set.
    10% Test set.
2. Define a time series window generator that can handle the indexes and offsets and divide the windows of features into (feature, labels) pairs.
3. Define a compile:
    Metrics: Mean Absolute Error (MAE)
    Loss function: Mean Square Error (MSE)
    Optimizer: Adam Optimizer
Model Training

## Slide 23
4. Define the model:
    CNN
    RNN
Model Training

## Slide 24
5. Train the model using simulated data.
6. Implement TL
    Freeze the pre-trained CNN or RNN model layers
    Add new trainable layers (2 dense layers)
    Train the new layers
    Fine tune the model
Model Training

## Slide 25
Results
RNN-Real Data
Transfer Learning
(RNN pre-training model)
Moth-inspired Data:

## Slide 26
Results
Moth-inspired Data:
CNN-Real Data
Transfer Learning
(CNN pre-training model)

## Slide 27
Results
Bayesian-inference Data:
CNN-Real Data
Transfer Learning
(CNN pre-training model)

## Slide 28
Results
Fusion Data:
CNN-Real Data
Transfer Learning
(CNN pre-training model)

## Slide 29
Results
Bayesian-inference Data:
RNN-Real Data
Transfer Learning
(RNN pre-training model)

## Slide 30
Results
Fusion Data:
RNN-Real Data
Transfer Learning
(CNN pre-training model)

## Slide 31
The OSL robot is a very challenging.
CNN and RNN models using real data show very weak generalizations.
TL is implemented to train the model using the knowledge of the pre-trained model.
Transfer learning achieves better performance.
The real-world experiments are supposed to be conducted as one of the project deliverables.
  An issue of calling the DNN model file (.h5) in MATLAB code.
  Run-out of time
Conclusions
Notes: and it needs to take many variables into account such as the environment, and the search algorithms.
due to the lack of OSL robot real data.
(CNN or RNN model) that used similar data to the real data.
in terms of model generalization

## Slide 32
References
[1] Wang, L.. (2021). "Robotic Olfactory-Based Navigation with Mobile Robots". PhD Dissertations and Master's Theses. 623. https://commons.erau.edu/edt/623
[2] Chollet, F. (2018). Deep Learning with Python, Shelter Island, NY: Manning Publications Co.
[3] Recurrent Neural Networks (RNN) with Keras ¦ TensorFlow Core. (2022). Retrieved 9 August 2022, from https://www.tensorflow.org/guide/keras/rnn
[4] tf.keras.layers.LSTM ¦ TensorFlow Core v2.9.1. (2022). Retrieved 9 August 2022, from https://www.tensorflow.org/api_docs/python/tf/keras/layers/LSTM
[5] Sarkar, D. (2018), "Towards Data Science“. Retrieved 9 August 2022 from https://towardsdatascience.com/a-comprehensive-hands-on-guide-to-transfer-learning-with-real-world-applications-in-deep-learning-212bf3b2f27a.
[6] Time series forecasting ¦ TensorFlow Core. (2022). Retrieved 9 August 2022, from https://www.tensorflow.org/tutorials/structured_data/time_series

## Slide 33
JA
By:
Mohammed Alajaji
Thank you
Questions?